## Slide 1
Controller and Observer Design Using Active Disturbance Rejection Control
FINAL YEAR PROJECT MID TERM PPT PRESENTATION
Group Number: 11
Group Members:
Ritika Meena (20225076)
Ratan Kumar (20225074)
Project Mentor: Dr. Souradip De
Department: Electrical Engineering, MNNIT Allahabad

## Slide 2
Table of Contents
1.Introduction
2.Luenberger Observer
3.Importance of Disturbance Rejection
4.Different DOB Techniques
5.Active Disturbance Rejection Control (ADRC)
6.ADRC Explanation & Block Diagram
7.Mathematical Proof (Stability)
8.Problem 1: Temperature Control (First Order)
9.Problem 2: DC-DC Buck Converter (Second Order)
10.Results & Discussion

## Slide 3
Introduction
Challenges in Control Systems:
-> Real-world systems face model uncertainties
and unknown external disturbances.
-> These factors degrade performance,
cause steady-state errors, and can lead to instability.
Limitations of Traditional Control:
-> Methods like PID and LQR rely heavily on an accurate
mathematical model of the plant.
-> Performance significantly deteriorates when the real system
deviates from the model.
Our Objective:
-> To design a robust observer-based control framework for effective disturbance estimation and rejection.
-> minimizing dependency on a precise plant model.
Test Systems: 1.Temperature Control (First-Order System)
2.DC-DC Buck Converter (Second-Order System)

## Slide 4
Luenberger Observer
Core Idea: Estimate the internal states of a system using only its outputs and inputs.
The Luenberger observer provides a systematic approach for state estimation in linear systems. For a linear time-invariant system:
where is the state vectoris the input, and is the output.
Observer Structure : The Luenberger observer is constructed as:
= C
where is the estimated state and L is the observer gain matrix.
Error Dynamics :
The estimation error e = − evolves according to:
The observer gain L is designed such that (A−LC) is Hurwitz (all eigen values have negative real parts), ensuring exponential convergence of the estimation error to zero.

## Slide 5
Why Disturbance Rejection is Important
Types of Disturbances:
1.External: Load changes, ambient variations, measurement noise
2.Internal: Parameter drift, unmodeled dynamics, nonlinearities
3.Structured: Known form but unknown magnitude
4.Unstructured: Completely unknown characteristics
The Impact:
1.Degrades performance & accuracy
2.Causes steady-state errors
3.Can lead to instability
Our Goal: Maintain performance and stability despite these unknowns

## Slide 6
Disturbance Observer (DOB) Techniques
Classical DOB:
Uses inverse of nominal plant model
Effective but sensitive to model inaccuracies
Requires relatively accurate system model
Extended State Observer (ESO):
Core of ADRC approach
Treats total disturbance as an extended state
Estimates both system states AND disturbances simultaneously
Key Advantage of ESO:
Doesn't need precise plant model
Only requires approximate input gain b₀
More robust to model uncertainties

## Slide 7
Active Disturbance Rejection Control (ADRC)
Core Philosophy: "Forget the detailed model - just estimate and cancel the total disturbance in real-time"
Three Key Components:
Tracking Differentiator (TD)
  Provides smooth reference signal
  Avoids setpoint jumps
Extended State Observer (ESO)
  Estimates system states + total disturbance
  Heart of the ADRC approach
Nonlinear State Error Feedback
  Generates control signal
  Often simplified to linear PD controller
Our Focus: Linear ADRC variant for practical implementation

## Slide 8
ADRC Explanation & Block Diagram
Simplified Plant Model:
f(t): "Total Disturbance" (all uncertainties)
b₀: Approximate input gain (only parameter needed)
Control Law:
Actively cancels disturbances
Transforms plant to pure integrator
Result: Robust control with minimal modelling effort

## Slide 9
Mathematical Proof - Stability Analysis
Lyapunov Stability Proof
Define the estimation error: e = − =
The error dynamics are:
Key Insight: ESO estimates both system states and total disturbance simultaneously
Choose a quadratic Lyapunov candidate
The time derivative is bounded by:
Assuming bounded disturbance derivative
This proves Uniform Ultimate Boundedness (UUB) and Input-to-State Stability (ISS).

## Slide 10
Problem 1 – Temperature Control System
Temperature Control in Real Life & Industry
Homes: room heaters, ovens, geysers → used daily for comfort and convenience.
Industries: furnaces, dryers, chemical reactors, food processing → temperature must be precisely maintained for safety, quality, and efficiency.
Objective: Maintain the object’s/room’s/process temperature at a desired value, despite changing environmental conditions.
System Variables (Control System View):
Controlled Variable (y): Object/room temperature → the quantity we want to regulate.
Manipulated Variable (u): Heater input power → the quantity we can directly change.
Disturbance: Ambient temperature → external factor that influences temperature but is not under our control.
Core Idea:
The heater supplies energy → raises object/room temperature.
Heat is lost to the environment through convection & radiation.
Ambient conditions () act as disturbances (like cold air in winter).
A controller (like a thermostat) adjusts to keep close to the desired setpoint.

## Slide 11
Energy Balance Principle
The rate of heat stored in the object = Heat supplied – Heat lost
Where:
: Mass of object (kg)
: Specific heat capacity (J/kgK)
: Object temperature (°C or K)
: Heater input power (W)
Heat Loss Mechanisms
1. Convection Loss
: Surface area of object (m²)
: Overall heat transfer coefficient (W/m²·K)
: Ambient temperature Linear dependence on temperature difference.
2. Radiation Loss
: Emissivity (0–1)
: Stefan–Boltzmann constant Nonlinear due to the term.

## Slide 12
Control System Representation
The original heat balance equation is nonlinear and contains uncertainties(radiation etc)
For control design, we need a simpler, linear-like structure.
This motivates the control system representation using a virtual disturbance and input gain.
Simplified Model Equation
Where:
→ Output
  This is the controlled variable, i.e., the temperature of the object or room.
→ Input
  This is the manipulated variable, i.e., the heater power we can adjust.
→ Virtual disturbance
  Includes all unmeasured effects, e.g.,
    Ambient temperature changes
    Nonlinear radiation losses
    Modelling inaccuracies
  Treated as a single disturbance term to simplify design.
→ Input gain
  Relates the heater input to the temperature rise
  Can be obtained from:
    Physical parameters (mass, specific heat, surface area)
    Step-response experiment
    Determines sensitivity of output to input.

## Slide 13
Simulation Results
PID Controller Performance (Red Line):
1.It is slower to settle at the target, taking about 240 seconds.
2.It overshoots the target by a significant amount (12.5%), meaning it heats up to almost 90°C before coming back down.
3.It is less accurate overall, with a higher Root Mean Square Error (RMSE: 0.45°C).
2.ADRC Controller Performance (Blue Line):
1.It is much faster, settling at the target in about 135 seconds.
2.It has a very small overshoot (4.2%), staying much closer to the desired 80°C.
3.It is more accurate, with a much lower error (RMSE: 0.15°C).
3.Key Difference in Behavior:
1.The PID controller reacts to disturbances and overshoots after they happen.
2.The ADRC anticipates and compensates for disturbances (like heat loss), resulting in a smoother, faster, and more stable response.

## Slide 14
Disturbance Estimation Performance
1. Actual System Disturbance(Black Line)::
Magnitude: -5 °C/s cooling effect
Timing: 600s to 900s (300-second duration)
Effect: Removes heat from the system
2. Observer Performance(Blue Line):
Accuracy: Successfully estimates the -5 °C/s disturbance
Response: Tracks the actual disturbance closely in real-time
Duration: Correctly identifies the exact 300-second disturbance period
3. Control Significance: This accurate estimation enables the ADRC controller to automatically counteract the cooling effect, maintaining the target temperature of 80°C despite the external disturbance.

## Slide 15
Control effort comparison for temperature regulation
Controller | Behaviour | Power Range | Energy Efficiency
ADRC (Blue) | Smooth, stable control action | 300-500W | Higher - Minimal energy waste
PID (Red) | Oscillatory, aggressive adjustments | 200-700W | Lower - Constant over-correction wastes energy
Control Effort Comparison: ADRC vs PID

## Slide 16
Problem 2 – Buck Converter(DC-DC Converter)
What is a Buck Converter?
-A type of DC-DC step-down converter that reduces an input DC voltage (to a lower regulated output ().
-Operates through high-frequency switching of a semiconductor device (MOSFET/IGBT) and uses passive components (inductor , capacitor ) to filter energy.
Why Buck Converter for Modelling?
-Simple yet representative topology for understanding DC-DC converter dynamics.
-Exhibits second-order system Behaviour(inductor current + capacitor voltage).
-Provides an ideal case study for plant modelling and testing ADRC (Active Disturbance Rejection Control) strategies.
Key State Variables:
-: Inductor current (energy storage in magnetic field).
: Capacitor voltage (energy storage in electric field).
-Both states define system dynamics and are used in control-oriented models.
Applications:
  Power supplies for electronic devices.
  Renewable energy systems (solar PV, wind).
  Electric vehicle (EV) powertrains and battery management.
  Embedded and industrial electronics requiring regulated DC power.

## Slide 17
Luenberger observer:
2nd order transfer function :
Simplified Plant Model:
Control Law:
Where:

## Slide 18
Output voltage regulation: ADRC vs PID controller
Parameter | ADRC | PID | Improvement
Voltage Regulation | ±0.5% | ±2.1% | 76% better
Settling Time | 2.5 ms | 8.2 ms | 70% faster
Efficiency | 94.2% | 91.5% | +2.7%
-ADRC maintains tighter voltage control (±0.5% vs ±2.1%)
-ADRC responds 3x faster to disturbances (2.5ms vs 8.2ms)
-ADRC achieves higher power efficiency (94.2% vs 91.5%)
Disturbance Estimation Performance
Parameter | Value | Significance
Estimation Accuracy | RMSE: 0.50 | High precision tracking
Observer Type | Luenberger Observer | Real-time disturbance detection
Performance | Effective Disturbance Rejection | Enables automatic compensation

## Slide 19
Parameter | ADRC (Blue) | PID (Red) | Advantage
Current Ripple | ±0.1A | ±0.3A | ADRC: 67% smaller ripple
Current Range | 1.2-1.4A | 1.0-1.6A | ADRC: Tighter control
Power Losses | Reduced | Increased | ADRC: Lower losses
Efficiency | Better (94.2%) | Lower (91.5%) | ADRC: +2.7% efficiency
Inductor Current Performance Comparison

## Slide 20
DC-DC Converter Results
Control Signal Performance Comparison
Parameter | ADRC (Blue) | PID (Red) | Advantage
Duty Cycle Range | 48-52% | 45-55% | ADRC: 40% smaller variation
Oscillations | Minimal | Significant | ADRC: Smother operation
Control Effort | Low | High | ADRC: More efficient
Stability | Better | Reduced | ADRC: Superior performance

## Slide 21
Results & Discussion :
Controller | RMSE (°C) | Settling Time (s) | Overshoot (%) | Robustness
PID | 0.440 | 244 | 12.6 | Low
ADRC (Proposed) | 0.209 | 158 | 5.1 | High
1.Temperature Control vs PID Controller
2.DC-DC Converter Performance Comparison
Controller | Regulation (%) | Settling Time (ms) | Efficiency (%)
PID | ±2.1 | 8.2 | 91.5
ADRC (Proposed) | ±0.5 | 2.5 | 94.2
Observation: The ADRC controller achieves lower RMSE, reduced settling time, and minimal overshoot compared to the conventional PID controller, indicating superior robustness and accuracy.
Observation: The proposed ADRC-based controller improves voltage regulation, speeds up transient response, and enhances efficiency, showing clear performance gains over the PID controller.

## Slide 22
Future Plans:
• MIMO Extension: Extend the hybrid DOB-ADRC architecture to Multi-InputMulti-Output (MIMO) systems with coupled dynamics for more complex applications.
• Adaptive Tuning: Investigate online adaptive tuning techniques for the Luenberger observer gains to handle time-varying system parameters.
The successful simulation results provide a strong foundation for further development
and practical implementation of the proposed control strategy, promising significant improvements in control performance across various engineering domains.

## Slide 23
THANK YOU !